## Slide 1: Supervoxel-Based Hierarchical Markov Random Field Framework for Multi-Atlas Segmentation
Ning Yu1, Hongzhi Wang2 and Paul A Yushkevich3
1:Department of Computer Science, University of Virginia 2:IBM Almaden Research Center 3:Penn Image Computing and Science Laboratory, Department of Radiology, University of Pennsylvania
MICCAI 2016 PATCH-MI Workshop
October 17, 2016, Athens Greece
This research is supported by NIH grant R01 EB017255

## Slide 2: Overview
Our prior work on joint label fusion
  Works great when you can do dense deformable registration
Can we do label fusion without dense deformable registration?
  Supervoxel matching without spatial context
  Supervoxel matching with discrete MRF registration (“new” method)
Initial results and further thoughts…

## Slide 3: ”Conventional” multi-atlas segmentation involves dense deformable registration
Atlas j
Target
ANTS, IRTK, LDDMM, etc.

## Slide 4: Label fusion by similarity-weighted voting
target image
atlas image 1
atlas image n
target
warped atlas 1
warped atlas k
similarity map
similarity map
weight map
weight map

## Slide 5: Redundancy in similarity-weighted label fusion
µ=2
µ=2
µ=2
µ=4
Total weight:
Daughter: 0.6
Son: 0.5
Notes: redundanica

## Slide 6
Joint Label Fusion (Wang et al., IEEE-PAMI 2013): Account for correlation/redundancy between atlases
target image
atlas image 1
atlas image n
target image
atlas image 1
atlas image n
voting map 1
voting map n
pairwise correlations are considered
voting map 1
voting map n
Independent label fusion
Joint label fusion
Notes: Related to Tumer and Ghosh, 1995 work on correlation in ensemble classifiers

## Slide 7: Joint Label Fusion formulation: at each voxel, find atlas weights that minimize expected total segmentation error
Wang et al., IPMI 2011, IEEE PAMI 2012

## Slide 8: Formulation: find vector of atlas weights that minimizes expected total segmentation error
Wang et al., IPMI 2011, IEEE PAMI 2012

## Slide 9: Corrective learning (Wang et al., 2011): a wrapper method to improve the performance of existing segmentation algorithms using training data
Wang et al., Neuroimage, 2011
Notes: Aprende de conocer y corregir
Patrones de desacuerdo
Voxeles mal etiquetados

## Slide 10: Joint label fusion yields outstanding segmentation performance especially when combined with additional voxel-wise intensity-based error correction (Wang et al., 2011)
Manual
Joint label fusion
Joint label fusion + corrective learning
Input image
Warfield, Landmann et al., MICCAI 2012 Multi-Atlas Labeling Challenge
Notes: Consurso de segmentaction en MICCAI

## Slide 11
ASHS: A multi-atlas pipeline optimized for labeling the hippocampal region in high-resolution T2-weighted MRI
Inputs:
  High-resolution T2-w MRI
  1mm resolution T1-w MRI
Algorithms:
  ANTS deformable registration1
  Joint label fusion2
  Corrective learning3
Output:
  Segmentation of hippocampal subfields and MTL cortices in the space of the T2-w MRI
1: Avants et al., MedIA, 2006; 2: Wang et al., Pattern Anal Mach Intell, 2012; 3: Wang et al., Neuroimage, 2011

## Slide 12
ASHS Performance vs. Manual Segmentation
1cm
Yushkevich et al., Human Brain Mapping,2014
Notes: Here is one case shows the average performance of ASHS.
The overall performance is competitive with inter rater manual segmentation reliability.
However, the thick slice posts challenge to shape analysis and thickness measurement.
PY: edited title to emph. That performance is vs. manual segmentation

## Slide 13: Joint label fusion without dense deformable registration
95-99% of computational time is spent in registration
  Only a fraction of the information in the deformation field is used for the fusion process
Diffeomorphic constraints may be too restrictive
  Don’t make sense in presence of lesions, etc.

## Slide 14: A spectrum of approaches for generating candidate matches for a target voxel
A patch in the target image
How to find good candidate matches in the atlas library for the voxel at the center of this patch?
Atlas library
?
Deformable Registration
PatchMatch (Coupe et al., 2014)
SuperVoxel MRF
Affine registration with local patch search (Coupe et al., 2010)
SuperVoxel matching (Wang et al., 2013)
Global search over all patches in all atlases
Amount of Spatial Context

## Slide 15: Wang et al., 2013 MICCAI: Label Transfer via Supervoxel Matching
Search space of candidate patches for a given target voxel is reduced by global supervoxel matching
  Atlas and target image divided into supervoxels
  Supervoxels most similar to the target supervoxel are found (based on attribute vector)
  Patches from selected supervoxels are used for voxel-level joint label fusion
atlas
atlas
target
Target SV
atlas SV
atlas SV
atlas SV
Notes: Work in Schnabel somewhere

## Slide 16: Wang et al., 2013 MICCAI: Label Transfer via Supervoxel Matching
Search space of candidate patches for a given target voxel is reduced by global supervoxel matching
  Atlas and target image divided into supervoxels
  Supervoxels most similar to the target supervoxel are found (based on attribute vector)
  Patches from selected supervoxels are used for voxel-level joint label fusion
Method largely serves as a proof of concept that joint label fusion can be applied without registration
  Allowed label fusion segmentation of brain tumors
  Fails for most problems where spatial context is needed for segmentation
Notes: Work in Schnabel somewhere

## Slide 17: Proposed method: SV matching with spatial context
Affine alignment
  To get corresponding anatomy roughly into place
Supervoxel oversegmentation (atlas and target)
  Uses the SLIC algorithm – supervoxels of consistent size and shape
Discrete MRF supervoxel registration
  Uses FastPD to quickly match supervoxels respecting spatial relationships
Voxel-level refinement
  Patch-based joint label fusion with MRF prior
  Learning-based error correction

## Slide 18: Details of the method
supervoxel-level pre-segmentation
atlases
N3 correction
FLIRT affine registration
histogram matching
supervoxel generation
target image
N3 correction
FLIRT affine registration
histogram matching
supervoxel generation
supervoxel-level MRF
voxel-level kNN
joint label fusion
voxel-level MRF
supervoxels
supervoxels
supervoxel correspondences as prior knowledge
label transfer
label probability distribution
final segmentation
atlases pre-processing
target image pre-processing
voxel-level refinement
learning-based error correction
training samples
start
start
end

## Slide 19: Details of the method
atlases
N3 correction
FLIRT affine registration
histogram matching
supervoxel generation
target image
N3 correction
FLIRT affine registration
histogram matching
supervoxel generation
supervoxel-level MRF
voxel-level kNN
joint label fusion
voxel-level MRF
supervoxels
supervoxels
supervoxel correspondences as prior knowledge
label transfer
label probability distribution
final segmentation
atlases pre-processing
target image pre-processing
supervoxel-level pre-segmentation
voxel-level refinement
learning-based error correction
training samples
start
start
end

## Slide 20: Details of the method
atlases
N3 correction
FLIRT affine registration
histogram matching
supervoxel generation
target image
N3 correction
FLIRT affine registration
histogram matching
supervoxel generation
supervoxel-level MRF
voxel-level kNN
joint label fusion
voxel-level MRF
supervoxels
supervoxels
supervoxel correspondences as prior knowledge
label transfer
label probability distribution
final segmentation
atlases pre-processing
target image pre-processing
supervoxel-level pre-segmentation
voxel-level refinement
learning-based error correction
training samples
start
start
end

## Slide 21: Supervoxel correspondence matching
Recent related work:
  Kanavati et al., MLMI 2015
    Finds correspondences between supervoxels in two images using random forests
    Can serve to initialize dense registration or for multi-atlas segmentation
    No spatial prior on the correspondence field
  Heinrich et al., MedIA 2016
    Multiple supervoxel graphs
    Discrete MRF-based supervoxel registration
    Unifies registration and label fusion

## Slide 22: Discrete MRF-based supervoxel matching
target image T
atlas A
P
Q
Data term: how similar is supervoxel P to the supervoxel in atlas A pointed to by
  Binary potential: how similar are displacements at adjacent supervoxels
  P,Q; weighted by the proximity and area of border between P and Q.
Search space: discrete set of displacements from target supervoxel centers
Minimized using FastPD (Glocker et al. 2008)

## Slide 23: Details of the method
atlases
N3 correction
FLIRT affine registration
histogram matching
supervoxel generation
target image
N3 correction
FLIRT affine registration
histogram matching
supervoxel generation
supervoxel-level MRF
voxel-level kNN
joint label fusion
voxel-level MRF
supervoxels
supervoxels
supervoxel correspondences as prior knowledge
label transfer
label probability distribution
final segmentation
atlases pre-processing
target image pre-processing
supervoxel-level pre-segmentation
voxel-level refinement
learning-based error correction
training samples
start
start
end

## Slide 24: Evaluation: multi-label diencephalon segmentation MICCAI 2013 SATA Challenge Dataset (Asman et al., 2013)
35 atlases, 12 testing images, 14 labels
T1
Supervoxels
Supervoxel-level pre-segmentation
Final segmentation
Ground truth

## Slide 25: Evaluation: multi-label diencephalon segmentation MICCAI 2013 SATA Challenge (Asman et al., 2013)
Leave-one-out segmentation accuracy relative to manual segmentation on the (n=35) training set

## Slide 26: Experiments: Effectiveness of SV-Level MRF
Supervoxel Level
Voxel Level
Average DSC
Average DSC
Wang et al., 2013 supervoxel method
Barnes et al. 2009 applied to SVs
Our approach
Straw man
JLF without MRF regularization
Our approach

## Slide 27: Experiments: Trade-Off between Accuracy and Efficiency
Evaluation on the SATA test dataset
Only 5s in FastPD
In parallel on a cluster

## Slide 28: Discussion and Conclusions
Seeding JLF with fast supervoxel matching can approach the accuracy of multi-atlas segmentation with dense deformable registration
  There is potential to speed up segmentation time by orders of magnitude
    Only 5s spent in FastPD algorithm, most of the time spent preprocessing
  Important to validate in more relevant and challenging problems
    E.g., body CT segmentation, where diffeomorphic registration assumptions may not hold
  Can the method be useful for segmenting pathology?

## Slide 29: Thank you!
Email: pauly2@upenn.edu
Web: http://picsl.upenn.edu

## Slide 30
T1
Supervoxels
Supervoxel-level pre-segmentation
Final segmentation
Ground truth

## Slide 31: Method: Pre-Processing
For both atlas and target images
  N3 correction
     homogeneity
  Affine registration to ICBM152 via FLIRT
     spatial regularization
     fast but low accuracy
  Histogram matching to ICBM152
     intensity regularization

## Slide 32: Method: Supervoxel-Level Pre-Segmentation
Why supervoxels?
  Adhering to natural boundaries >> regular patches
  Compact and concise representation >> voxels
  Robust label transfer >> voxel label transfer
  Narrowing down valid regions for voxel-level refinement

## Slide 33: Method: Voxel-Level Refinement
MRF solver: FastPD [Glocker et al., MedIA 2008]
 Supervoxel pair to each of atlases
 Supervoxel label transfer: majority voting
 Only consider voxels inside valid target supervoxels
 kNN voxel-surrounding patch neighbors
 Voxel label transfer: joint label fusion [Wang et al., PAMI 2013]
 Label probability vector vp(lp)
Data term
  Smoothness term